## Slide 1: Handling multidimensional arrays and sparse matrices

## Slide 2: Stride: Handling Multidimensional Arrays in Vector Architectures
The position in memory of adjacent elements in a vector may not be sequential. Consider this straightforward code for matrix multiply in C:
  for (i = 0; i < 100; i=i+1)
  for (j = 0; j < 100; j=j+1) {
  A[i][j] = 0.0;
  for (k = 0; k < 100; k=k+1)
  A[i][j] = A[i][j] + B[i][k] * D[k][j]; }
We could vectorize the multiplication of each row of B with each column of D and strip-mine the inner loop with k as the index variable.
To do so, we must consider how to address adjacent elements in B and adjacent elements in D.
When an array is allocated memory, it is linearized and must be laid out in either row-major (as in C) or column-major (as in Fortran) order.

## Slide 3: Stride: Handling Multidimensional Arrays in Vector Architectures
This linearization means that either the elements in the row or the elements in the column are not adjacent in memory.
For example, the C code above allocates in row-major order, so the elements of D that are accessed by iterations in the inner loop are separated by the row size times 8 (the number of bytes per entry) for a total of 800 bytes.
This distance, separating elements to be gathered into a single register is called the stride.
In this example, matrix D has a stride of 100 double words (800 bytes), and matrix B would have a stride of 1 double word (8 bytes).
For column-major order, which is used by Fortran, the strides would be reversed. Matrix D would have a stride of 1, or 1 double word (8 bytes), separating successive elements, while matrix B would have a stride of 100, or 100 double words (800 bytes).

## Slide 4: Stride: Handling Multidimensional Arrays in Vector Architectures
Once a vector is loaded into a vector register, it acts as if it had logically adjacent elements. Thus, a vector processor can handle strides greater than one, called non-unit strides, using only vector load and vector store operations with stride capability.
This ability to access nonsequential memory locations and to reshape them into a dense structure is one of the major advantages of a vector processor.
On VMIPS, where the addressable unit is a byte, the stride for our example would be 800. The value must be computed dynamically, since the size of the matrix may not be known at compile time or—just like vector length—may change for different executions of the same statement.

## Slide 5: Stride: Handling Multidimensional Arrays in Vector Architectures
The vector stride, like the vector starting address, can be put in a general-purpose register. Then the VMIPS instruction LVWS (load vector with stride) fetches the vector into a vector register.
Like- wise, when storing a non-unit stride vector, use the instruction SVWS (store vector with stride).
Supporting strides greater than one complicates the memory system. Once we introduce non-unit strides, it becomes possible to request accesses from the same bank frequently. When multiple accesses contend for a bank, a memory bank conflict occurs, thereby stalling one access. A bank conflict and, hence, a stall will occur if

## Slide 6: Stride: Handling Multidimensional Arrays in Vector Architectures
Suppose we have 8 memory banks with a bank busy time of 6 clocks and a total memory latency of 12 cycles. How long will it take to complete a 64-element vector load with a stride of 1? With a stride of 32?
Since the number of banks is larger than the bank busy time, for a stride of 1 the load will take 12 + 64 = 76 clock cycles, or 1.2 clock cycles per element.
The worst possible stride is a value that is a multiple of the number of memory banks, as in this case with a stride of 32 and 8 memory banks. Every access to memory (after the first one) will collide with the previous access and will have to wait for the 6-clock-cycle bank busy time. The total time will be 12 + 1 + 6 * 63 = 391 clock cycles, or 6.1 clock cycles per element.

## Slide 7: Gather-Scatter: Handling Sparse Matrices in Vector Architectures
In a sparse matrix, the elements of a vector are usually stored in some compacted form and then accessed indirectly. Assuming a simplified sparse structure, we might see code that looks like this:
for (i = 0; i < n; i=i+1)
A[K[i]] = A[K[i]] + C[M[i]];
This code implements a sparse vector sum on the arrays A and C, using index vectors K and M to designate the nonzero elements of A and C. (A and C must have the same number of nonzero elements—n of them—so K and M are the same size.) The primary mechanism for supporting sparse matrices is gather-scatter operations using index vectors. The goal of such operations is to support moving between a compressed representation (i.e., zeros are not included) and normal representation (i.e., the zeros are included) of a sparse matrix.
A gather operation takes an index vector and fetches the vector whose elements are at the addresses given by adding a base

## Slide 8: Gather-Scatter: Handling Sparse Matrices in Vector Architectures
address to the offsets given in the index vector. The result is a dense vector in a vector register. After these elements are operated on in dense form, the sparse vector can be stored in expanded form by a scatter store, using the same index vector.
Hardware support for such operations is called gather-scatter and it appears on nearly all modern vector processors.
The VMIPS instructions are LVI (load vector indexed or gather) and SVI (store vector indexed or scatter).
For example, if Ra, Rc, Rk, and Rm contain the starting addresses of the vectors in the previous sequence, we can code the inner loop with vector instructions such as:

## Slide 9: Gather-Scatter: Handling Sparse Matrices in Vector Architectures
This technique allows code with sparse matrices to run in vector mode.
A programmer directive would tell the compiler that it was safe to run the loop in vector mode.
Although indexed loads and stores (gather and scatter) can be pipelined, they typically run much more slowly than non-indexed loads or stores, since the memory banks are not known at the start of the instruction.
Each element has an individual address, so they can’t be handled in groups, and there can be conflicts at many places throughout the memory system. Thus, each individual access incurs significant latency.